;	Programme de test pour la liaison I²C

;************************************************************

LIST P=18F452

#include <P18F452.INC>

list	n=0	; suppress list file page breaks

list	ST=off	; suppress list file symbol table

;************************************************************

; Register File Assignment

EEADDR		equ	0x000	; Address register

EEDATA		equ	0x001	; data to read/write

EESLAVE		equ	0x002	; Device address (1010xxxy)

DelayCtr1	equ	0x003	; delay routine counter

DelayCtr2	equ	0x004	; delay routine counter

SlaveAddr	equ	0xA0	; slave address literal

;************************************************************

; Vector Assignment

ORG	0x00000

goto	Start	; Reset Vector

;************************************************************

; Main Program			prgr Principal

ORG	0x00040		; Start of Program space

Start

; initialize PORTB

clrf	LATB		; Clear PORTB output latch

clrf	TRISB		; Set PORTB as all outputs

; configure SSP for hardware master mode I2C

bsf	SSPSTAT,SMP	; I2C slew rate control disabled

bsf	SSPCON1,SSPM3	; I2C master mode in hardware

bsf	SSPCON1,SSPEN	; enable SSP module

movlw	0x09		; set I2C clock rate to 100kHz

movwf	SSPADD

bsf	TRISC,3		; I2C SCL pin is input

bsf	PORTC,3		; (will be controlled by SSP)

bsf	TRISC,4		; I2C SDA pin is input

bsf	PORTC,4		; (will be controlled by SSP)

movlw	SlaveAddr	; EEPROM I2C address

movwf	EESLAVE

Main				prgr

clrf	PORTB		; initialize variables

clrf	EEDATA

clrf	EEADDR

WrEEPROM			prgr d’écriture

bsf	PORTB,7		; indicate write, light TX LED

rcall	Delay

bcf	EESLAVE,0	; write mode

rcall	WakeSlave	; gets slave attention

rcall	WrADDR		; sends EEPROM address

rcall	WrDATA		; sends data to slave

rcall	Stop		; send stop bit

incf	PORTB,F		; increment count

incf	EEDATA,F	; increment data

incf	EEADDR,F	; Point to next address

btfss	EEADDR,7	; at end of EEPROM?

goto	WrEEPROM	; no, write more data

RdLoop

clrf	PORTB		; initialize variables

clrf	EEDATA

clrf	EEADDR

RdEEPROM			prgr de lecture

rcall	Delay

bcf	EESLAVE,0	; write mode

rcall	WakeSlave	; gets slave attention

rcall	WrADDR		; sends EEPROM address

rcall	Stop		; send stop bit

bsf	EESLAVE,0	; read mode

rcall	WakeSlave	; gets slave attention

rcall	RdDATA		; receive one data byte, leaves idle

movf	EEDATA,W	; get data

movwf	PORTB		; move received data to PORTB

xorwf	EEADDR,W	; compare data with address

bz	GoodData	; branch if DATA = ADDR

rcall	Errorloop	; DATA is wrong, indicate error

GoodData			prgr de vérification

incf	EEADDR,F	; Point to next address

btfss	EEADDR,7	; at end of EEPROM?

goto	RdEEPROM	; no, read more data

goto	Main		; do it all over again

;************************************************************

; TX LED flashes to indicate error while displaying received data.

;Errorloop			prgr d’affichage donnée trasmise mauvaise

;rcall	Delay

;btg	PORTB,7		; Toggle TX LED

;rcall	Delay

;btg	PORTB,7		; Toggle TX LED

;rcall	Delay

;btg	PORTB,7		; Toggle TX LED

;rcall	Delay

;btg	PORTB,7		; Toggle TX LED

;rcall	Delay

;btg	PORTB,7		; Toggle TX LED

;rcall	Delay

;btg	PORTB,7		; Toggle sTX LED

;return

;************************************************************

; sends start bit, slave address

; if ACK not recieved, sends restart, tries again

; execution can get stuck in this loop if slave not present

; can be used to poll slave status (retries until slave responds)

WakeSlave			ss- prgr Evoi du bit de start

bsf	SSPCON2,SEN	; Send start bit

btfsc	SSPCON2,SEN	; Has SEN cleared yet?

goto	$-2		; No, loop back to test.

rWakeSlave

bcf	PIR1,SSPIF	; clear interrupt flag

nop

movf	EESLAVE,W

movwf	SSPBUF		; move slave address to SSPBUF

btfss	PIR1,SSPIF		; has SSP completed sending SLAVE Address?

goto	$-2		; no, loop back to test

btfss	SSPCON2,ACKSTAT	; was ACK received from slave?

return			; yes, return to calling routine

bsf	SSPCON2,RSEN	; send repeated start bit

btfsc	SSPCON2,RSEN	; has repeated start been sent yet?

goto	$-2		; no, loop back to test

bra	rWakeSlave	; send slave address again

;************************************************************

; writes EEPROM memory address, hangs if no ACK

WrADDR				ss- prgr Ecriture de l’adresse

bcf	PIR1,SSPIF	; clear interrupt flag

movff	EEADDR,SSPBUF	; move EEPROM address to SSPBUF

btfss	PIR1,SSPIF	; has SSP completed sending EEPROM Address?

goto	$-2		; no, loop back to test

btfsc	SSPCON2,ACKSTAT	; has slave sent ACK?

goto	$-2		; no, try again

return

;************************************************************

; Sends one byte of data to slave, hangs if no ACK

WrDATA				ss- prgr Ecriture de la donnée

bcf	PIR1,SSPIF	; clear interrupt flag

movff	EEDATA,SSPBUF	; move data to SSPBUF

btfss	PIR1,SSPIF	; has SSP completed sending data to EEPROM?

goto	$-2		; no, loop back to test

btfsc	SSPCON2,ACKSTAT	; has slave sent ACK?

goto	$-2		; no, try again

return

;************************************************************

; receive one byte from slave

; do not send ACK, send stop bit instead

RdDATA			ss- prgr Ecriture de la donnée

bcf	PIR1,SSPIF	; clear interrupt flag

bsf	SSPCON2,RCEN	; enable receive mode

btfss	PIR1,SSPIF	; has SSP received a data byte?

goto	$-2		; no, loop back to test

bsf	SSPCON2,ACKDT	; no ACK

bsf	SSPCON2,ACKEN	; send ACKDT bit

btfsc	SSPCON2,ACKEN	; has ACKDT bit been sent yet?

goto	$-2		; no, loop back to test

bsf	SSPCON2,PEN	; send stop bit

btfsc	SSPCON2,PEN	; has stop bit been sent?

goto	$-2		; no, loop back to test

movff	SSPBUF,EEDATA	; save data to RAM

bcf	SSPCON2,RCEN	; disable receive mode

return

;************************************************************

; Sends stop bit, waits until sent

Stop			ss- prgr Evoi du bit de stop

bsf	SSPCON2,PEN	; send stop bit

btfsc	SSPCON2,PEN	; has stop bit been sent?

goto	$-2		; no, loop back to test

return

;************************************************************

; a delay of 98.57mS

Delay			ss- prgr Tempo

movlw	0x80

movwf	DelayCtr2	; preset

clrf	DelayCtr1	; clear counter

Delay1

decfsz	DelayCtr1	; decrement counter

bra	Delay1		; back to top of loop

decfsz	DelayCtr2	; decrement counter

bra	Delay1		; back to top of loop

return

END